VirtualLab
Introduction
VirtualLab (VL) is a python package which enables the user to run Finite Element (FE) simulations completely via the command line. The pre and post processing is carried out using the software SALOME, while the FE solver CodeAster is used for the simulation. While this package has been written for command line use some capabilites have been included to use the GUI for debugging and training.

Layout
VirtualLab contains three essential directories needed for running any simulation; ‘Scripts’, ‘Materials’ and ‘Input’. There is also a ‘Run’ file which is used to launch simulations.
Scripts – This directory contains all of the scripts needed to set up VirtualLab, the SALOME scripts and CodeAster command files. The sub-directory ‘Common’ contains everything needed to set-up a study, such as creating directories and inerfacing with SALOME and CodeAster. There is also a sub-directory for each simulation type (which is currently Tensile, LFA and HIVE). Inside each of these sub-directories is the relevant SALOME and CodeAster files to run that specific simulation. Each has a PreProc, Aster and PostProc directory containing the relevant scripts. This directory also contains other simulation-specific subdirectories, I.e. ‘Laser’ for LFA which contains different laser pulse profiles.
Materials – This directory contains the material properties which will be used for FE simulations. The sub-directories are different materials, each of which contain material properties. Some materials are non-linear with temperature dependence.
Input – The Input directory contains the parameters which will be used for running simulations, such as dimensions to create a mesh and boundary conditions and materials for FE simulations. Input has a sub-directory for each simulation, and within each of those you will find sub-directories for different study directories (this will be explained more in the next section).

Getting Started
To use VirtualLab there are a few things which must be set up. The first is that you have both SALOME and CodeAster installed on your computer. Once this is done you need to add the SALOME directory to your path so that salome can be opened by just typing ‘salome’ in a terminal window. Talk to Llion
There are also a couple of packages which are needed and are designated in the Setup.sh script (These are h5py for dealing with SALOME’s .med files and iapws which is needed for HIVE simulations). If there are any issues please see http://docs.h5py.org/en/stable/build.html and https://pypi.org/project/iapws/)

The results generated by VL are written to the Output directory in the top level directory (this will be created once simulations are run). The location of the Output directory can be changed to another location through the VlConfig.py file however for this training material it is advisable to leave this in its default location. There are 4 arguments which must be defined to use VL; Simulation, StudyDir, StudyName, Input.

Simulation – This indicated the type of simulation which will be run; Tensile, LFA or HIVE. A directory of the Simulation will be created in the Output directory.
StudyDir – This is a sub directory of Simulation to keep things organised, i.e. here you could specify a type of component you are testing, such as ‘MetalBar’. In this directory also you will find the directory ‘Meshes’ where all the meshes for this type of Study will be saved.
StudyName – A sub-directory of StudyDir where Simulations results will be stored. This is specific to the set of Simulations you are running. For example if you are testing out different magnitude of loads, you could name this ‘LoadingAnalysis’.
Inputs – This dictionary defines the name of the file(s) containing the information required to create a mesh and/or run a simulation. The dictionary must always have the key ‘Parameters’ which defines the main parameter file. If no other argument is provided a single simulation will be run using the information from this file. If the key ‘Parametric’ is included in the dictionary it is possible to run multiple simulations con-currently with different parameters. The ‘Parameters’ file and ‘Parametric’ file must be in the directory Inputs/$SIMULATION/$STUDYDIR
You will also notice when the class is initialised a key-word argument ‘mode’ is passed – this dictates how much information is printed in the terminal. There are 3 different options available; headless (default), continuous and interactive. Interactive will output all commands in to the terminal, continuous will write the output to a file as it is generated, and headless will write the output in to the file at the end of the process. The output for the meshing stage can be found in the ‘Meshes’ directory, while the output for each CodeAster simulation can be found in the ‘Aster’ directory for each specific Study. For the below tasks it is advised to keep the mode as ‘interactive’ so that you can see the outputs generated by VL easily.

Mechanical FE – Tensile Test
The first topic for the training is running a mechanical FE simulation of a standard tensile test with a ‘Dog-Bone’ sample. In these experiments it is possible to load the sample either with a constant force or enforce a constant displacement. In the VL Tensile Test both of these methods are available. For simplicity this is a purely elastic simulation.
Task 1
For this task the Run.py file should be set up already. However the 4 variables in the Run file should be:
Simulation = 'Tensile'
StudyDir = 'Example'
StudyName = 'Training'
Input = {'Parameters' : 'TrainingParameters’}
The first step is to open the Parameters file ‘TrainingParameters.py’ which can be found in Inputs/Tensile/Example. You will notice a Namespace called ‘Mesh’ which defines the geometrical and meshing parameters. The file which is used to create the mesh is defined at Mesh.File, which in this case is ‘Testpiece’. This file can be found in Scripts/Tensile/PreProc. The attributes of Mesh, such as Thickness, are passed to this file to create a mesh named ‘Notch1’ which will be saved in Output/Tensile/Example/Meshes. You will also notice a Namespace named ‘Sim’ which has all the information relevant to run pre-simulation calculations, the simulation and post-processing calculations and images. As you can see the Name attached to ‘Sim’ is ‘Single’, meaning that the results for this simulation will be in Output/Tensile/Example/Training/Single.

As previously mentioned it is possible to perform a constant force and/or a constand displacement simulation. As you can see the dictionary for Sim.Load in the parameters file shows that both types of tensile tests will be performed on the sample provided, with the magnitude for each provided as they keys.

Execute the Run.py file, where you should see a mesh named ‘Notch1’ being created followed by a Simulation named ‘Single’ showing up in an xterm terminal.

Since the kwarg ‘ShowRes’ is set to ‘True’ in VirtualLab.PostProc in the Run file the results are automatically opened in ParaVis for you to take a look at. There should be two sets of results shown: one for a constant force simulation and another for a constant displacement simulation.

Task 2
The next step is to run multiple simulations at the same time. Change the Input dictionary to include the key, value pair ‘Parametric’,’Parametric_1’ (your Input dictionary should now look like Input={'Parameters' : 'TrainingParameters', 'Parametric' : 'Parametric_1'}). What we are now saying is that we use the file ‘Parametric_1.py’ (also in Inputs/Tensile/Example) in conjunction with the parameters file to create multiple parameter files. If a variable is defined in the parametric file then this value is used, however if the variable is not defined the value from the parameters file will be used. For example, in ‘Parametric_1’ you will see that 2 meshes are being created (‘Notch2’ and ‘Notch3’) with different values for Rad_a and Rad_b, however the thickness of the sample will still be 0.003 since this is what is defined in ‘TrainingParameters’ and it is not specified in the parametric file.

Execute the Run file and you should see meshes ‘Notch2’ and ‘Notch3’ are created along with 2 xterm terminals opening, one for each simulation. The names of the simulation (‘ParametricSim1’ and ‘ParametricSim2’) are written at the top of the xterm window to differntiate them.

Task 3
You realise after running the simulation that the wrong Material was set in the Parameters file. You wanted to run a simulation on a Tungsten testpiece not a copper one. You are happy with the meshes you already have for ‘Notch 2’ and ‘Notch 3’ and don’t want to re-run the meshing step. In the Run file in VirtualLab.Create write ‘RunMesh=False’. This will switch off the meshing part and only run the Simulation (There is also a kwarg RunSim’ also exists and works in the same way as RunMesh for the simulation). Change the Material in the Parameters file to ‘Tungsten’ and Run the simulation. You should notice the displacement is smaller for the tungsten sample compared with copper (for the contant force simulation).

Once you have completed the above tasks it may be worthwhile you looking at the files which have been used to create this simulations. See Scripts/Tensile/Preproc/DogBone.py which has been used to make the mesh and the CodeAster command file in Scripts/Tensile/Aster/Tensile.comm. Take a look at these to try and figure out what each part is doing.

Thermal FE – Laser Flash Analysis
The next topic for the training is to run a thermal FE simulations of a Laser Flash Analysis (LFA) experiment. In this experiment a small disc is subjected to a short laser pulse on the top surface. The simulation shows how the temperature profile of the disc changes with time due to the energy input from the laser pulse. Radiation effects are ignored in this simulation to verify that the conservation of energy is satisfied.

Task 1
As this is a new simulation type you will need to change ‘Simulation’ in the Run file to ‘LFA’. You will also need to remove ‘RunMesh=False’ fromVirtualLab.Create (or set the flag to ‘True’) since new meshes will need to be created. The variables in the Run file should be:
Simulation = 'LFA'
StudyDir = 'Example'
StudyName = 'Training'
Input = {'Parameters' : 'TrainingParameters’, ‘Parametric’:’Parametric_1’}

If you open TrainingParameters.py and Parametric.py in Inputs/LFA/Example you can see that 2 meshes are being created, ‘NoVoid’ and ‘Void’, and 3 simulations are run, 1 using the mesh ‘NoVoid’ (‘SimNoVoid’) and 2 using the mesh ‘Void’ (‘SimVoid1’ & ‘SimVoid2’). As this is a time-dependent problem you will notice that there are some additional variables in the ‘Sim’ namespace relating to that.
Sim.dt - Sim.dt dictates the time-steps used for the simulation. For this example you have Sim.dt=[(0.00004,20), (0.0005,100)], meaning that there will be 20 timesteps of size 0.00004 and then100 timesteps of size 0.0005. The initial smaller timesteps is to reflect the fac that the laser pulse will last for 0.0008s.
Sim.Theta – The value of theta sites between 0 and 1 and is used to decide whether the temporal idscretisation is fully explicit (Theta=0), fully implicit (Theta=1) or semi-implicit (0<Theta<1).
Sim.Storing – This variable decides how frequently we want to store the results with regards to the timesteps. In this example The key ‘Laser’ has a value 1 and ‘PostLaser’ has a value 2, meaning that the results will be stored after every 1 timestep for the duration of the laser pulse, and after every 2 timesteps after the laser pulse.This means that there will be 70 timesteps saved to the .rmed file (20/1+100/2). For this simulation there are post-processing scripts which have been written already, so change the ‘ShowRes’ flag in VirtualLab.PostAster to ‘False’.

Execute the Run.py file. After it has completed if you look in Output/LFA/Example/Training you should see the 3 simulation directories. In the Aster directory for each simulation you have the AsterLog, Export File and .rmed file(s) as seen in the Tensile example. As this is a time-dependent problem you will notice a file of the timesteps used for the simulaition is also saved. This holds the full list of 120 timesteps used for the simualtion. If you look in the PostAster directory you will notice there are a number of plots showing the temperature distribtuion with respect to time, and images of the sample with a heat distribution shown. Images of the mesh used are also included.

Task 2
After running Task1 you realise that you wanted to run the simulation ‘NoVoid’ with a uniform laser profile, not a gaussian one. To re-run certain studies from a parametric study there is a way this can be done quickly and easily. In the Parametric file if you include Sim.Run = [‘Y’,’N’,’N’] this will signal that we only want to Run the first simulation (The default is that it assumes that all simulations are a ‘Y’). Add this line to ‘Parametric_1.py’ and change the first value in Sim.LaserS to ‘Uniform’. You should also set RunMesh to False in VirtualLab.Create() since we are happy to use the meshes created previously.

Task 2