VirtualLab
Introduction
VirtualLab (VL) is a python package which enables the user to run Finite Element (FE) simulations completely via the command line. The pre and post processing is carried out using the software SALOME, while the FE solver CodeAster is used for the simulation. While this package has been written for command line use some capabilites have been included to use the GUI for debugging and training.

Layout
VirtualLab contains three essential directories needed for running any simulation; ‘Scripts’, ‘Materials’ and ‘Input’. There is also a ‘Run’ file which is used to launch simulations.
Scripts – This directory contains all of the scripts needed to set up VirtualLab, the SALOME scripts and CodeAster command files. The sub-directory ‘Common’ contains everything needed to set-up a study, such as creating directories and inerfacing with SALOME and CodeAster. There is also a sub-directory for each simulation type (which is currently Tensile, LFA and HIVE). Inside each of these sub-directories is the relevant SALOME and CodeAster files to run that specific simulation. Each has a PreProc, Aster and PostProc directory containing the relevant scripts. This directory also contains other simulation-specific subdirectories, I.e. ‘Laser’ for LFA which contains different laser pulse profiles.
Materials – This directory contains the material properties which will be used for FE simulations. The sub-directories are different materials, each of which contain material properties. Some materials are non-linear with temperature dependence.
Input – The Input directory contains the parameters which will be used for running simulations, such as dimensions to create a mesh and boundary conditions and materials for FE simulations. Input has a sub-directory for each simulation, and within each of those you will find sub-directories for different study directories (this will be explained more in the next section).

Getting Started
To use VirtualLab there are a few things which must be set up. The first is that you have both SALOME and CodeAster installed on your computer. Once this is done you need to add the SALOME directory to your path so that salome can be opened by just typing ‘salome’ in a terminal window. Talk to Llion
There are also a couple of packages which are needed and are designated in the Setup.sh script (These are h5py for dealing with SALOME’s .med files and iapws which is needed for HIVE simulations). If there are any issues please see http://docs.h5py.org/en/stable/build.html and https://pypi.org/project/iapws/)

The results generated by VL are written to the Output directory in the top level directory (this will be created once simulations are run). The location of the Output directory can be changed to another location through the VlConfig.py file however for this training material it is advisable to leave this in its default location. There are 4 arguments which must be defined to use VL; Simulation, StudyDir, StudyName, Input.

Simulation – This indicated the type of simulation which will be run; Tensile, LFA or HIVE. A directory of the Simulation will be created in the Output directory.
StudyDir – This is a sub directory of Simulation to keep things organised, i.e. here you could specify a type of component you are testing, such as ‘MetalBar’. In this directory also you will find the directory ‘Meshes’ where all the meshes for this type of Study will be saved.
StudyName – A sub-directory of StudyDir where Simulations results will be stored. This is specific to the set of Simulations you are running. For example if you are testing out different magnitude of loads, you could name this ‘LoadingAnalysis’.
Inputs – This dictionary defines the name of the file(s) containing the information required to create a mesh and/or run a simulation. The dictionary must always have the key ‘Parameters’ which defines the main parameter file. If no other argument is provided a single simulation will be run using the information from this file. If the key ‘Parametric’ is included in the dictionary it is possible to run multiple simulations con-currently with different parameters. The ‘Parameters’ file and ‘Parametric’ file must be in the directory Inputs/$SIMULATION/$STUDYDIR
You will also notice when the class is initialised a key-word argument ‘mode’ is passed – this dictates how much information is printed in the terminal. There are 3 different options available; headless (default), continuous and interactive. Interactive will output all commands in to the terminal, continuous will write the output to a file as it is generated, and headless will write the output in to the file at the end of the process. The output for the meshing stage can be found in the ‘Meshes’ directory, while the output for each CodeAster simulation can be found in the ‘Aster’ directory for each specific Study. For the below tasks it is advised to keep the mode as ‘interactive’ so that you can see the outputs generated by VL easily.

Mechanical FE – Tensile Test
The first topic for the training is running a mechanical FE simulation of a standard tensile test with a ‘Dog-Bone’ sample. In these experiments it is possible to load the sample either with a constant force or enforce a constant displacement. In the VL Tensile Test both of these methods are available. For simplicity this is a purely elastic simulation.
Open the Parameters file ‘TrainingParameters.py’ which can be found in Inputs/Tensile/Example. You will notice a Namespace called ‘Mesh’ which defines the necessary geometrical dimensions and meshing parameters needed to create a mesh. The file which is used to create the mesh is defined at Mesh.File, which in this case is ‘DogBone’. This file can be found in Scripts/Tensile/PreProc. The attributes of Mesh, such as Thickness, are passed to this file to create a mesh named ‘Notch1’ which will be saved in Output/Tensile/Example/Meshes. You will also notice a Namespace named ‘Sim’ which has all the information relevant to run pre-simulation calculations, the simulation and post-processing calculations and imaging. As you can see the Name attached to ‘Sim’ is ‘Single’, meaning that the results for this simulation will be in Output/Tensile/Example/Training/Single.

Task 1
For this task the Run.py file should be set up already. However the 4 variables in the Run file should be:
Simulation = 'Tensile'
StudyDir = 'Example'
StudyName = 'Training'
Input = {'Parameters' : 'TrainingParameters’}
As previously mentioned it is possible to perform a constant force and/or a constand displacement simulation. As you can see the dictionary for Sim.Load in the parameters file shows that both types of tensile tests will be performed on the sample provided, with the magnitude for each provided as they keys.

Execute the Run.py file, where you should see a mesh named ‘Notch1’ being created followed by a Simulation named ‘Single’ showing up in an xterm terminal (you will need to exit out of the terminal once the simulation has completed).

Since the kwarg ‘ShowRes’ is set to ‘True’ in VirtualLab.PostProc in the Run file the results are automatically opened in ParaVis for you to take a look at. There should be two sets of results shown: one for a constant force simulation and another for a constant displacement simulation.

Task 2
The next step is to run multiple simulations at the same time. Change the Input dictionary to include the key, value pair ‘Parametric’,’Parametric_1’ (your Input dictionary should now look like Input={'Parameters' : 'TrainingParameters', 'Parametric' : 'Parametric_1'}). What we are now saying is that we use the file ‘Parametric_1.py’ (also in Inputs/Tensile/Example) in conjunction with the parameters file to create multiple parameter files. If a variable is defined in the parametric file then this value is used, however if the variable is not defined the value from the parameters file will be used. For example, in ‘Parametric_1’ you will see that 2 meshes are being created (‘Notch2’ and ‘Notch3’) with different values for Rad_a and Rad_b, however the thickness of the sample will still be 0.003 since this is what is defined in ‘TrainingParameters’ and it is not specified in the parametric file.

Execute the Run file and you should see meshes ‘Notch2’ and ‘Notch3’ are created along with 2 xterm terminals opening, one for each simulation. The names of the simulation (‘ParametricSim1’ and ‘ParametricSim2’) are written at the top of the xterm window to differntiate them.

Task 3
You realise after running the simulation that the wrong Material was set in the Parameters file. You wanted to run a simulation on a tungsten testpiece, not copper. You are happy with the meshes you already have for ‘Notch 2’ and ‘Notch 3’ and don’t want to re-run the meshing step. In the Run file in VirtualLab.Create write ‘RunMesh=False’. This will switch off the meshing part and only run the Simulation (There is also a kwarg RunSim’ also exists and works in the same way as RunMesh for the simulation). Change the Material in the Parameters file to ‘Tungsten’ and Run the simulation. You should notice the displacement is smaller for the tungsten sample compared with copper (for the contant force simulation).

Once you have completed the above tasks it is worthwhile to look at the files which have been used to create this simulations. See Scripts/Tensile/Preproc/DogBone.py which has been used to make the mesh and the CodeAster command file in Scripts/Tensile/Aster/Tensile.comm. Take a look at these to try and figure out what each part is doing.

Thermal FE – Laser Flash Analysis
The next topic for the training is to run a thermal FE simulations of a Laser Flash Analysis (LFA) experiment. In this experiment a small disc is subjected to a short laser pulse on the top surface. The simulation shows how the temperature profile of the disc changes with time due to the energy input from the laser pulse. Radiation effects are ignored in this simulation to verify that the conservation of energy is satisfied.

As this is a new simulation type you will need to change ‘Simulation’ in the Run file to ‘LFA’. You will also need to remove ‘RunMesh=False’ fromVirtualLab.Create (or set the flag to ‘True’) since new meshes will need to be created. If you open TrainingParameters.py in nputs/LFA/Example you will notice there are extra parameters in the Sim namespace due to the time-dependent nature of the experiment:

Sim.dt –This indicates the time-steps used for the simulation. Given that the laser pulse chosen for this simulation is ‘Trim’ which lasts for 0.0004 we require a finer timestepping during the initial 0.0004s. For this example you have Sim.dt=[(0.00002,20,1), (0.0005,100,2)], meaning that there will be 20 timesteps of size 0.00002 followed by 100 timesteps of size 0.0005. The 3rd variable in each tuple indicated how often we want to store the results (if no 3rd variable is passed the default value is 1). For the first 20 timesteps we will store each result, and thereafter we will store every second result. This means that there will be 71 results at different points at time saved to the .rmed file – The initial condition, 20/1 and 100/2.

Sim.Theta – The value of theta sites between 0 and 1 and is used to decide whether the temporal idscretisation is fully explicit (Theta=0), fully implicit (Theta=1) or semi-implicit (0<Theta<1).

Task 1
The variables in the Run file should be:
Simulation = 'LFA'
StudyDir = 'Example'
StudyName = 'Training'
Input = {'Parameters' : 'TrainingParameters’, ‘Parametric’:’Parametric_1’}

If you open Parametric_1.py you will see that 2 meshes are being created, ‘NoVoid’ and ‘Void’, and 3 simulations are run, 1 using the mesh ‘NoVoid’ (‘SimNoVoid’) and 2 using the mesh ‘Void’ (‘SimVoid1’ & ‘SimVoid2’). You are interested in seeing the meshes which are created before running the simulation. In VirtualLab.Mesh enter the kwarg ‘ShowMesh = True’. This will open all the meshes created in the GUI for you to take a look at to asses their suitability. Once you close the GUI the script will terminate (That is no simulaton will run).

Task 2
You are happy with the quality of the meshes created for your simulation, so the next step is to run the simulation. Since we are happy with the meshes created we can remove the kwarg ‘ShowMesh’ and set the RunMesh flag to False in VirtualLab.Create. For this simulation there are post-processing scripts which have been written already, so change the ‘ShowRes’ flag in VirtualLab.PostAster to ‘False’ (Or remove it altogether since the default value is False).

Execute the Run.py file. After it has completed if you look in Output/LFA/Example/Training you should see the 3 simulation directories. In the Aster directory for each simulation you have the AsterLog, Export File and .rmed file(s) as seen in the Tensile example. As this is a time-dependent problem you will notice a file of the timesteps used for the simulaition is also saved. This holds the full list of 120 timesteps used for the simualtion. If you look in the PostAster directory you will notice there are a number of plots showing the temperature distribtuion with respect to time, and images of the sample with a heat distribution shown. Images of the mesh used are also included. You will notice there is a plot named ‘Rplot’ which plots the transient average temperature on different sized areas of the bottom surface. For example R=1 takes an average over the entire bottom surface, while R=0.5 takes the average of values within half of the Radius of the bottom surface. Notice that for ‘SimVoVoid’ R=0.1 increases fastest due to the Gaussian profile of the laser pulse, however ‘SimVoid2’ R=0.1 increases slowest due to the void providing a thermal barrier. The different values for R are given in the Parameters file (R=1 is always included in this plot for comparison).

Task 3
You want to run the post-processing for the simulations again with different values for R. Since the simulations results you already have don’t need to change there’r no need to re-run the simulation. In VirtualLab.Aster enter the kwarg ‘RunAster = False’, which indicates that the Aster part doesn’t need to run. Try new values of R (between 0 and 1) and execute the Run script again.

Task 4
You realise that you wanted to run the simulation ‘NoVoid’ with a uniform laser profile, not a gaussian one. To re-run certain studies from a parametric study there is a way this can be done quickly and easily. In the Parametric file if you include Sim.Run = [‘Y’,’N’,’N’] this will signal that we only want to Run the first simulation (The default is that it assumes that all simulations are a ‘Y’). Add this line to ‘Parametric_1.py’ (There is no need to have the Sim.Run variable in ‘TrainingParameters’ file) and change the first value in Sim.LaserS to ‘Uniform’. Remember that you will need to change ‘RunAster’ back to True (or remove it since True is the default value).

Task 5
You will have noticed that the CodeAster command file used for the LFA simulations so far was ‘Disc_Lin’, which is a linear simulation. There is also a command file called Disc_NonLin available which allows us to use non-linear material properties (i.e. material properties which vary with temperature). In the ‘Materials’ directory you will notice that there are some non-linear materials available (those with NL after them). Re-run the simulations with the CommFile set to Disc_NonLin. You should also change the materials to a non-linear material also (although the simulation will still work if a linear material is provided).

You will notice that the CodeAster output looks different for the non-linear simulation compared with the linear simulation. This is due to the fact that the non-linear simulations require performing Newton iterations on each timestep, which is not required in the linear case. The default maximum numbr of Newton iterations is 10, however this can be changed by adding ‘MaxIter’ to the Sim Namespace in the Parameters file. For the meshes and timesteps used for this simulation 10 Newton iterations should be sufficient.